Part - B

Financial Bid

TENDER FOR POLYCARBONATE ROOFING WORK OVER PERGOLA FOR OLD IV-D HOUSING QUARTERS.

at

Inter-University Centre for Astronomy and Astrophysics

# Post Bag -4, Ganeshkhind, Pune University Campus,

Pune 411 007.

Bill of Quantities (BOQ)

Financial Bid

“TENDER FOR POLYCARBONATE ROOFING WORK OVER PERGOLA FOR OLD IV-D HOUSING QUARTERS, AT IUCAA, PUNE”

THE INTER UNIVERSITY CENTER FOR ASTRONOMY & ASTROPHYSICS (IUCAA)

POST BAG 4, GANESHKHIND, PUNE UNIVERSITY CAMPUS,

PUNE 411 007, INDIA

Name of Work   : 	             			ROOFING WORK  –  AT IUCAA

A.	Name of Vendor  / Firm / Company		____________________________

____________________________

Postal Address				       	  ____________________________

____________________________

Telephone Off.					____________________________

Telex / Fax						____________________________

Email ID						____________________________

Signature & seal of Bidder

| INTER-UNIVERSITY CENTRE FOR ASTRONOMY AND ASTROPHYSICS |
| --- |
| PROJECT : POLYCARBONATE ROOFING WORK OVER PERGOLA FOR IV D OLD QUARTERS AT S. NO. 25/1/1/1/1/B, HOUSING SITE AT IUCAA CAMPUS, GANESHKHIND, PUNE |
| BILL OF QUANTITIES |
| Sr No. | Item Description | Qty | Unit | Rate | Amount in Rs. |
| 1 | Removing of existing FRP sheet and structural steel |  |  |  |  |
|  | Removing of existing FRP sheets and supported MS structural steel members from the second floor level, cutting, removing exiting base plate / anchor fasteners, making the area ready for providing new pergola and stacking them near the substation area as directed by the Engineer in charge. Agency has to come and visit the exact place of work before quoting the rates. The item will be paid on the per unit basis of houses. | 12 | Units |  |  |
| 2 | Polycarbonate Roofing |  |  |  |  |
|  | Providing & fixing 10 mm thick lexan polycarbonate multiwall clear Bronz sheets to the MS frame with special powder coated top section on joint with double EPDM gaskets, bottom section with EPDM double gaskets with DC 995 structural silicon sealant 6mm thick double sided Adhesive tape with aluminium anticapilary end section, self drilling screw with EPDM rubber washers & multi foil antisaging two way 3m make cushion tape with proper slopes. (The actual finished area of sheets shall be taken for calculation of billing). 20.83 Sqm. X 12 Units | 250 | SQM. |  |  |
| 3 | Fabrication |  |  |  |  |
|  | Providing & fixing with required fabrication MS tubulor frame to support the polycarbonate roofing of Tata SHS/RHS pipes with necessary base plate, fastner bolts, cement grouting, cleats, tie etc. at required level including finishing the end with end plate, griding and two coates of black Asian make satin finished paint on one coat of Asian make zinc primer. Cost to include the safety devises, sattubelts, safety belt where ever necessary.The actual structural steel used will be measured for payment. No payment will be made for wastage / balance material. | 5 | M.T. |  |  |
| 4 | Kemperol waterproof membrane V210 |  |  |  |  |
|  | Providing kemperol V210 type waterproof membrane of 300cm wide at the junction of masonary wall and roofing sheets with kemperol primer, kemperol V210 resin, polyester reinforcing fleece, V210 resin as per technical specifications of the manufacturer complete as directed by Engineering In-Charge. | 100 | R.M. |  |  |
| TOTAL AMOUNT |  |
| (Amount in Words : ___________________________________________________________________ ) |
| Stamp and Sign.of the contractor) |